## Slide 1
PITWALL
Tyre degradation intelligence
Forecast the pace risk.
Price the response.
Aditya & Ruhani / TrackShift 2026
Notes: PITWALL / TrackShift 2026. Present the app using Present to jury. This deck accompanies the working local demo; all metrics come from artifacts/demo/intelligence/*.json. Do not claim a validated optimal pit lap or places gained.

## Slide 2
Tyre wear is hidden inside lap pace
Fuel + tyres + traffic + track evolution
−0.154
Naive HARD slope / s per lap
+0.063
After confounder correction
A plausible practice curve still failed the race-transfer test.
We validate race forecasting and stop scenarios separately.
Historical research at tyre age 10; not a direct physical wear sensor.
Notes: Source: artifacts/demo/model.json → degradation_curves.practice.compounds.HARD. Slopes evaluated at tyre age 10. Historical research artifacts predate the replay traffic correction. The practice-to-race transfer failed; these are identification evidence, not deployed physical wear estimates.

## Slide 3
Lock the forecast. Then reveal the lap.
HUNGARY / NOR / LAP 25 → LAP 28
LOCKED FORECAST
85.066s
ACTUAL LAP
85.071s
ABSOLUTE ERROR
0.005s
Persistence error: 0.098s. The forecast stays fixed as replay advances.
One historical example. The next benchmark includes every scored evaluation forecast.
Notes: Source: artifacts/demo/intelligence/R11.json. Snapshot NOR / lap 25 / horizon 3; target lap 28. Demo example uses the pre-existing default cursor, not a search for best error. Prediction 85.066332; actual 85.071; persistence 84.973. One example is not an accuracy claim. In app: Present to jury → Predict & verify → Advance to lap 28 & score.

## Slide 4
Traffic can erase the undercut margin
3.95s tyre benefit − 0.08s rival pace − 1.50s gap − 0.70s warm-up
+1.67s
Central margin / clean rejoin
-0.33s
With 2s of rejoin traffic
Both stress ranges cross zero. The tool exposes a fragile attack
instead of inventing a confident pit command.
Both cars stop; shared pit transit cancels. Costs and inventory require engineer input.
Notes: Sources: artifacts/demo/intelligence/R11.json stop_scenarios.HARD and battles[horizon=3] at NOR lap25. Scenario: 1.5s gap, 0.7s warm-up, equal service, zero extra degradation, both cars stop. Central margin = 3*1.315561 - 0.078218 -1.5 -0.7 =1.668465s. Adding 2s total rejoin traffic gives -0.331535s. Combined stress radius =3*2.032157 +2.497010 =8.593481s. Conditional arithmetic, no validated overtake claim.

## Slide 5
Measured improvement against baselines
Chart: 
| Pace forecast | Rival-time forecast
PITWALL | 0.74282 | 2.1971
Baseline | 0.84365 | 2.4419
12.0%
less pace RMSE
10.0%
less rival-time RMSE
6,831 pace and 3,128 rival forecasts. Four reused evaluation races.
Stop-step RMSE 0.757s vs 0.761s: too small a gain to claim optimal pit strategy.
Notes: Sources: artifacts/demo/intelligence/report.json and battle_report.json. Pace RMSE on 6831 forecasts; relative-time RMSE on3128 forecasts. All later-race results use earlier-race fits. Architectures selected using development events; R09-R12 are reused evaluation events. Forecasts assume same-stint green running.

## Slide 6
A decision aid the engineer can inspect
01 Predict and verify the next laps
02 Stress the undercut with traffic and rival response
03 Inspect the baseline, coverage and model limits
Measured forecast advantage. Transparent strategy assumptions.
Grounded engineer briefing. Offline replay.
Open the app → Present to jury
Notes: Sources: current local application demo_fallback/index.html; docs/JURY_PRESENTATION.md; artifacts/demo/intelligence/*.json. Use the app four-chapter walkthrough. Strong claims are forecast accuracy and inspectable scenario arithmetic; physical tyre life, actual race time saved and positions won remain unproven.